## Slide 1: Low-to-high-quality seismic image translation using deep learning
Presented by: Ying Ting (Rhea) Lau
External supervisors from SLB UK: Dr. Rajiv Kumar, Dr. Massimiliano Vassallo
Internal supervisor from ETH Zurich: Dr. Dirk-Jan van Manen

## Slide 2: Seismic processing dilemma
OR
Raw
seismic gather
Standard quality
seismic gather
Low-cost
processing
Raw
seismic gather
High quality
seismic gather
High-cost processing
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 3: Is there a way do high-quality seismic processing fast and cheap?
Raw
seismic gather
Low-cost
processing
High quality
seismic gather
This is our thesis objective
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 4: Low-to-high-quality seismic image translation 2-step workflow
Selected raw
seismic gathers
Standard quality
seismic gathers
High quality
seismic gathers
Low-cost processing
High-cost processing
DL model training
Apply DL model
Step 1: Train a deep learning (DL) model with selected seismic gathers from both low-cost and high-cost processing
All raw
seismic gathers
Standard quality
seismic gathers
High quality
seismic gathers
Low-cost processing
Step 2: Applied the trained DL model to all low-cost processed seismic gathers
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 5: To test this workflow, we took seismic interpolation as an example
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 6: MPFI Matching Pursuit Fourier Interpolation
TDRI Time Domain Radon Interpolation
Interpolate traces by matching data iteratively in the Fourier domain
Interpolate traces by matching data iteratively in the Radon domain (intercept time and dip)
Standard industry solution, affordable
Limited robustness to spatial aliasing
More robust to aliasing, works on steeply
dipping events, overall better quality
Significantly more expensive

## Slide 7: Gulf of Mexico dataset
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: MPFI are more subjected to interpolation artifacts

## Slide 8: Seismic interpolation dilemma
OR
All raw
seismic gathers
Standard quality
seismic gathers
3D MPFI
All raw
seismic gathers
High quality
seismic gathers
3D TDRI
CPU time: 13 hours
CPU time: 127,294 hours
On a 3700 dataset, TDRI was nearly 10000 times more computationally expensive!!!
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: On 3700 km2 gulf of Mexico dataseet

## Slide 9: MPFI-to-TDRI seismic image translation 2-step workflow
Step 1: Train a deep learning (DL) model with ONE small subset of data from both MPFI and TDRI
Step 2: Applied the trained DL model to the whole dataset after MPFI to obtain pseudo TDRI results
One raw
seismic gather
MPFI
seismic gather
TDRI
seismic gather
3D MPFI
3D TDRI
All raw
seismic gathers
MPFI
seismic gathers
Pseudo TDRI
seismic gathers
3D MPFI
Apply DL model
DL model training
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 10: Create training data
2D Seismic Slices
Inline
Crossline
Time
3D Seismic Volume
256
256
Edge Patch
Edge Patch
Edge Patch
. . . . . .
. . . . . .
. . .
. . .
Patches are 50% overlapping in both directions
Zero padding
Zero padding
2D Seismic Slice
2D Seismic Slice
2D Patch
601
826
500
Edge patches are excluded in the training and validation set, but are included in the test set
6010 paired MPFI-TDRI patches as our data for model training
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: Receiver spaced 1000m source 50m, ideally we used both crossline and inlin
Edge patches has a lot of zero, maping zero to zero instead of amplitude to ampltide, remove instability in learning processes
ed

## Slide 11: Model training
Models are trained with Nvidia A100 GPUs
Hyperparameters are carefully selected for each model
We experimented 3 deep learning models:
Generative Adversarial Network (GAN)
Swin Transformer Convolutional Residual Network (SCRN)
Swin Transformer Convolutional Residual Generative Adversarial Network (SCR-GAN)
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: Initially the objective is to use GAN, I came up with the idea of SCRN, this is contribution

## Slide 12: What is GAN? Generative Adversarial Network
Generator
Discriminator
Embedding space
Fake Images
Real Images
Real or Fake
The Artist
The Critic
Loss and gradient backpropagation
Learn!
MPFI Images
Pseudo TDRI Images
TDRI Images
Model 1

## Slide 13: Generator and discriminator learn the features using convolutional neural network (CNN)
8 | -3 | 9 | -2
1 | 2 | 4 | 0
0 | 5 | -7 | 10
0 | 5 | 3 | 1
0 | -1
5 | 2
12 | 22
5 | 7
Convolutional layer involves applying a kernel filter over the input data and computing the dot product between the filter and the covered input area.
CNN captures local features well
Input data
Kernel filter
Output data
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 14: Generator and discriminator learn the features using convolutional neural network (CNN)
8 | -3 | 9 | -2
1 | 2 | 4 | 0
0 | 5 | -7 | 10
0 | 5 | 3 | 1
0 | -1
5 | 2
12 | 22
5 | 7

## Slide 15: GAN architecture
Reduction block
Convolution
Batch normalisation
Activation function
Dropout
Transposed convolution
Batch normalisation
Activation function
Dropout
Reduction block
Reduction block
Expansion block
Expansion block
Expansion block
Reduction block
Expansion block
Concatenation
Convolution
Transposed convolution
Flatten
Linear
Input
G Output
D Output
Repeat until the dimension becomes 1
Concatenation
Concatenation
Repeat until reaches the input dimension
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 16
Convolution
Batch normalisation
ReLU
CNN block
x3
Convolution
Split channels
Combine channels
Feature fusion block (FFB)
Convolution
Convolution
ViT
block
CNN
block
Input
Output
Convolution
Convolution
Repeat according to the layer configuration
What is SCRN? Swin Transformer Convolutional Residual Network
Model 2

## Slide 17: What is ViT? Vision Transformer
Patch Embedding
Patch Un-embedding
Encoder
Decoder
Patch Embedding
Encoder
Extract local feature of each patch
Analyse relationships between patches and capture the overall structure of the target
Decode using the feature learnt in the encoding part
Decoder
Patch Un-embedding
Reshape the decoder output into the image format
While CNN captures local features well, ViT captures global features well

## Slide 18
How about SCRN+GAN?
Model 3
Reduction block
Reduction block
Reduction block
Convolution
Flatten
Linear
Input
D Output
Repeat until the dimension becomes 1
Feature fusion block
Feature fusion block
Feature fusion block
Convolution
Feature fusion block
Convolution
G Output
Repeat according to
block configuration
Convolution
Batch normalisation
Activation function
Dropout
Reduction block
Convolution
Split channels
Combine channels
Feature fusion block (FFB)
Convolution
Convolution
ViT
block
CNN
block
Notes: I decide, this is the innovative part, this doesn’t exisit
Expand this part

## Slide 19: SCR-GAN
I proposed building a new architecture combining both GAN and SCRN
The presence of generator and discriminator makes the model more robust
ViT and CNN allow the model to capture both small scale features and long-range pixels relevant
ViT
block
CNN
block
Generator
Discriminator
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 20: Model evaluation metrics:
Performance on seen data
(Training dataset)
Performance on unseen data
(Validation dataset)
Generator/
Discriminator/
SCRN Loss
Signal-to-Noise Ratio
(SNR)
Training SNR
Validation SNR
Training Loss
Validation Loss
Lower loss and higher SNR indicates better model performance.
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: Quantitatively how we are doing, loss how well we are doing on the netwaork optimiser
SNR could be misleading as it can be high by matching the high amplitude

## Slide 21: Let’s compare our three models:
SCRN outperformed the other models
with the lowest loss and highest SNR.
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: Can use table

## Slide 22: How about the image translation performance? Let’s test it on an unseen common receiver gather

## Slide 23: Analyse the difference between the target value and reconstructed value
t = 4.6s
t = 4.6s
t = 4.6s
Edge patches are excluded in the training and validation set, but are included in the test set

## Slide 24: Analyse the reconstruction (1/3)
MPFI slice TDRI slice Pseudo TDRI (GAN) Pseudo TDRI (SCRN) Pseudo TDRI (SCRGAN)
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: Remove cross

## Slide 25: Difference with the target value (1/3)
MPFI - TDRI TDRI (GAN) - TDRI TDRI (SCRN) - TDRI TDRI (SCRGAN) - TDRI
Notes: Don’t circle it
Scrn based model did recognise aliasing better

## Slide 26: Analyse the reconstruction (2/3)
MPFI slice TDRI slice Pseudo TDRI (GAN) Pseudo TDRI (SCRN) Pseudo TDRI (SCRGAN)
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: TDRI is not physics blind, knows the dip range

## Slide 27: Difference with the target value (2/3)
MPFI - TDRI TDRI (GAN) - TDRI TDRI (SCRN) - TDRI TDRI (SCRGAN) - TDRI

## Slide 28: Analyse the reconstruction (3/3)
MPFI slice TDRI slice Pseudo TDRI (GAN) Pseudo TDRI (SCRN) Pseudo TDRI (SCRGAN)
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 29: Difference with the target value (3/3)
MPFI - TDRI TDRI (GAN) - TDRI TDRI (SCRN) - TDRI TDRI (SCRGAN) - TDRI

## Slide 30: Conclusion on our experiment
SCRN performs MPFI-TDRI image translation the best
Reconstructed TDRI images with high resemblance and denoising
Once trained, the SCRN model could produce TDRI quality result through the low-to-high quality translation workflow, with computational costs comparable to MPFI processing.
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 31: With new datasets available
Apply transfer learning: input new dataset to the trained model
After many updates, the network will be generalised to most area
Then we can exclude the training stage and apply SCRN directly
X
X
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: After many update, the network will be generalised to all are, transfer learning
For gulf of mexico

## Slide 32: Our ultimate goal is to apply this 2-step workflow on different seismic processing technologies, to get high quality result with low cost
Selected raw
seismic gathers
Standard quality
seismic gathers
High quality
seismic gathers
Low-cost processing
High-cost processing
DL model training
Apply DL model
All raw
seismic gathers
Standard quality
seismic gathers
High quality
seismic gathers
Low-cost processing
Step 1
Step 2
Now we have proven the feasibility of this workflow on seismic interpolation
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 33: Other applications example: Ocean bottom node (OBN) demultiple
Raw
seismic gather
UDD results
MDD results
UDD
MDD
DL model training
Step 1
Raw
seismic gather
Step 2
Apply DL model
High-cost
processing
Low-cost
processing
UDD results
UDD
Low-cost
processing
MDD results
OBN demultiple is typically achieved by deconvolving up-going and down going wavefield
Up-down deconvolution (UDD) is cheaper but requires a flat seabed
Multi-dimensional deconvolution (MDD) overcomes this limitation but involves severely higher costs
Conclusion
Other applications
Model evaluation
Experiment
Introduction
Notes: MDD requires stable interpolation across sparsely sampled receivers, significantly increasing the computational burden and complexity compared to UDD, which operates on common receiver gathers without such interpolation

## Slide 34: UDD-MDD translation
We experimented training the same SCRN model used for MPFI-TDRI experiment on the UDD-MDD dataset
Our preliminary results make us optimistic that UDD-MDD translation can be achieved with optimised hyperparameters
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 35: Thesis recap
Aim to upscale result from an affordable processing technology
Focus on interpolation, we explored the feasibility of the 2-step workflow
Prototyped and tested 3 deep learning models
  Two state-of-the-art architecture from recent literature: GAN, SCRN
  One novel architecture: SCR-GAN (patent application submitted)
Generalised to other applications, such as demultiple (patent application submitted)
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 36: Is there a way do high-quality seismic processing fast and cheap?
Raw
seismic gather
Low-cost
processing
High quality
seismic gather
Yes, there is!
By mapping low-cost processed data to high-quality results with deep learning.
Conclusion
Other applications
Model evaluation
Experiment
Introduction

## Slide 37: Low-to-high-quality seismic image translation using deep learning
Presented by: Ying Ting (Rhea) Lau
External supervisors from SLB UK: Dr. Rajiv Kumar, Dr. Massimiliano Vassallo
Internal supervisor from ETH Zurich: Dr. Dirk-Jan van Manen

## Slide 38: Limitations
Garbage in, garbage out
  The quality of image translation is capped by the quality of the data, if the data have noises, then the model will also learn them and output noises.
Limited data, limited generalisation
  Our model is trained exclusive to the Gulf of Mexico dataset. Getting pairs of MPFI and TDRI datasets are costly.

## Slide 39: Improvements
Weighting key traces for training
Expand the training data
Increase dataset variety through frequency augmentation

## Slide 40: Domains
Seismic wavelet’s energy is compact in time and spreads across frequencies,
such that the signal often appears as sparse, concentrated in a narrow range of τ values and specific dip, making it easier to distinguish from noise than in the frequency domain.

## Slide 41: MPFI algorithm

## Slide 42: TDRI algorithm

## Slide 43: Weighting key traces

## Slide 44: Model training time

## Slide 45: Model performance

## Slide 46: Model optimisation (GAN)

## Slide 47: Model optimisation (SCRN)

## Slide 48: Model parameters